How to Do Port Forwarding

If you want to access your IP Camera remotely, that is , viewing your camera from Internet., so port forwarding in your main router is necessary. The specific method of operation is as follows:

- Login your main router,(the main router means the first level router,in case you have 2 or more routers.), the common router address is http://192.168.1.1 or http://192.168.0.1,

- Login into the operater interface, find “Forwarding rules”option, “Virtual Servers”option.

- Fill in the camera IP address and port to the corresponding column,then save.

- Make the parameters take effects, then exit, as shown below:

To check whether you have done port forwarding successfully, you need to test it by yourself, find you external IP address, it can be found in your router or just search “my external IP” from Google Search, then put it in your browser with your camera port , for example,  http://119.136.186.102:2008

As we all  know, there are so many different routers, different brands, different models, but generally speaking, the settings are the same. Some other routers are shown below:

After finishing port forwarding and ddns settings, you are able to view your camera via DDNS.

For example:

http://wanscam1.ipcpnp.com:port number

(if port number is 80,you donot need to add this port number in link :hhttp://wanscam1.ipcpnp.com;

if port number is not 80,for example it is 88,http://wanscam1.ipcpnp.com:88  )

, user, user.

But you’d better use another computer from other network, sometimes it doesn't work in Lan.

Attention:When you have trouble in port forwarding , you can contact technical support(IPCamera&Router) or the Internet service provider.